## Slide 1
⚡ GridMind · HackSphere 3.0 · Zoho Catalyst
01 / 06
HACKSPHERE 3.0 · ZOHO CATALYST
GridMind
Smart Energy Microgrid & Demand Forecasting
Forecasts the next 24 hours of demand with Catalyst QuickML, switches between the main grid and battery storage, and warns before an overload.
RMSE
8.7 kW
R²
0.97
APPSAIL
LIVE

## Slide 2
PROBLEM STATEMENT
Every hour, a microgrid must pick its power source
⚡ GridMind · HackSphere 3.0 · Zoho Catalyst
02 / 06
Forecast
Predict hourly demand (kW) for the next 24 h from temperature, humidity and solar irradiance telemetry.
Switch
Use renewable battery storage when demand > 160 kW or during the 18:00–22:00 peak; otherwise the main grid.
Alert
Raise a critical overload alert for any hour forecast at or above 200 kW.
WHY IT'S HARD
92 → 215
kW, night vs evening peak
+8–11
kW per °C above 24 °C
−0.94
humidity ↔ temperature r
45.9 kW
starter baseline RMSE

## Slide 3
SOLUTION ARCHITECTURE
QuickML predicts, AppSail runs the rest
⚡ GridMind · HackSphere 3.0 · Zoho Catalyst
03 / 06
ZOHO CATALYST
Inputs
Browser: CSV, form, scenario predict.py evaluator
AppSail · Flask
Clean & validate feature builder (11 features)
QuickML
Linear Regression endpoint + SHAP explainer
Controller
Grid ↔ storage rules overload alerts
Battery sim
SoC, sizing advisor ₹ cost, CO₂
OAuth + endpoint key
Dashboard + /api/predict served from the same AppSail app — no separate Slate host, no cross-origin auth
Secrets stay server-side
OAuth refresh token + endpoint key live in AppSail env vars, never in the repo. Evaluators need no credentials.
Train/serve parity
One feature module builds the QuickML training CSV and every live request. Live endpoint within 0.83 kW of reference.
Honest degradation
Dashboard falls back to a local mirror model and says so; /api/predict returns 502 instead of faking QuickML.

## Slide 4
MODEL PERFORMANCE
Physics-informed features beat every tree model
⚡ GridMind · HackSphere 3.0 · Zoho Catalyst
04 / 06
RMSE
8.7 kW
QuickML test split
R²
0.97
QuickML test split
MAE
6.9 kW
QuickML test split
ROLLING-ORIGIN CV · RMSE kW ON UNSEEN FUTURE HOURS · LOWER IS BETTER
GridMind linear
8.96
Tuned boosting (raw)
9.93
Gradient boosting
10.23
Random forest
11.45
Default boosting (raw)
13.55
Starter baseline
45.94
Why linear wins: hourly base-load profile + cooling degrees above 24 °C split by time of day. Linear terms extrapolate into hotter test days; trees flatten out. 80% lower error than the starter baseline.

## Slide 5
LIVE DASHBOARD
From a forecast to an operating plan, in one screen
⚡ GridMind · HackSphere 3.0 · Zoho Catalyst
05 / 06
Battery SoC & sizing advisor
Hour-by-hour state of charge with solar charging; finds the smallest battery that covers every storage hour.
What-if temperature slider
Shift temperature −8 to +6 °C and watch load, alerts and the battery plan re-plan live.
Cost savings in ₹
Time-of-day tariffs vs running on the grid all day — ₹24,960 saved on the heatwave scenario.
CO₂ avoided
2.02 t avoided on the heatwave day from 1,216 kWh of solar.
Explainable + uncertain
QuickML SHAP attributions per hour, 90% intervals and P(overload).

## Slide 6
RESULTS
Deployed, verified, and ready to try
⚡ GridMind · HackSphere 3.0 · Zoho Catalyst
06 / 06
TEST_EVAL.PY
SUCCESS
1,000 predictions via QuickML
RMSE VS BASELINE
−80%
45.9 → 8.96 kW on future data
LIVE PARITY
0.83 kW
QuickML vs reference model
OVERLOADS FLAGGED
15 h
heatwave scenario, 275 kW peak
● TRY IT LIVE
gridmind-50047185567.development.catalystappsail.in
POST /api/predict · prediction API used by predict.py
GitHub github.com/yashviharia/GridMind
Pick “Heatwave day”, drag the what-if slider, click any hour for its explanation.